I2C_LCD_Library for I2C_PCF8574 \ A

This library uses the MikroC I2C1_Library function, all the commands are a carbon
copy of the MikroC Lcd_Library,
The differences are as follows:
  1. there is no need to define constant sbit's.
  2. I2C 1 module is used in this library.
  3. I2C1 module must be configured independently.
  4. All function arguments are unsigned char type.

### Library Routines
- I2C_Lcd_Init
- I2C_Lcd_Out
- I2C_Lcd_Chr
- I2C_Lcd_Cmd
I2C_Lcd_Init
Prototype	void Lcd_Init(unsigned char I2C_address);
Returns	Nothing.
Description	Initializes I2C_Lcd module to multi line no cursor.
Requires	Global variables: / I2C address of the the module to be defined as unsigned char / must be defined before using this function.
Example	Unsigned char LCD_01_ADDRESS = 0x7E; //0x7E is the address of / //PCF8574A with A0-2 at VSS / I2C_LCD_init(LCD_01_ADDRESS)

I2C_Lcd_Out
Prototype	void Lcd_Out(unsigned char row, unsigned char column, unsigned char *text);
Returns	Nothing.
Description	Prints text on Lcd starting from specified position. Both string variables and literals can be passed as a text. / Parameters : / I2C_address:the address of the I2C PCF8574 / A / row: starting position row number / column: starting position column number / text: text to be written
Requires	The Lcd module needs to be initialized. See I2C_Lcd_Init routine.
Example	// Write text "Hello!" on Lcd starting from row 1, column 3: / unsigned char LCD_01_ADDRESS = 0x7E; / I2C_Lcd_Out(LCD_01_ADDRESS,1, 3, "Hello!");

I2C_Lcd_Chr
Prototype	void Lcd_Chr(unsigned char I2C_Address, unsigned char row, unsigned char column, unsigned char out_char);
Returns	Nothing.
Description	Prints character on Lcd at specified position. Both variables and literals can be passed as a character. / Parameters : / I2C_address:the address of the I2C PCF8574 / A / row: writing position row number / column: writing position column number / out_char: character to be written
Requires	The Lcd module needs to be initialized. See I2C_Lcd_Init routine.
Example	// Write character "i" at row 2, column 3: / unsigned char LCD_01_ADDRESS = 0x7E; / I2C_Lcd_Chr(LCD_01_ADDRESS ,2, 3, 'i');

Prototype	void I2C_Lcd_Cmd(unsigned char I2C_Address ,Lcd Command,1);
Returns	Nothing.
Description	Sends command to Lcd. / Parameters : / I2C_address:the address of the I2C PCF8574 / A / Lcd Command: writing Lcd Command / constant: 1 has no value in this context as reuse of function for other cmd / Note : Predefined constants can be passed to the function, see Available Lcd Commands.
Requires	The Lcd module needs to be initialized. See I2C_Lcd_Init table.
Example	// Clear Lcd display: / unsigned char LCD_01_ADDRESS = 0x7E; / I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_CLEAR,1);

Available Lcd Commands / typedef enum{ Lcd Command}Cmd_Type; / extern Cmd_Type Cmd; //this enum variable must be declared in the main source code
Lcd Command	Purpose
_LCD_FIRST_ROW	Move cursor to the 1st row
_LCD_SECOND_ROW	Move cursor to the 2nd row
_LCD_THIRD_ROW	Move cursor to the 3rd row
_LCD_FOURTH_ROW	Move cursor to the 4th row
_LCD_CLEAR	Clear display
_LCD_RETURN_HOME	Return cursor to home position, returns a shifted display to its original position. Display data RAM is unaffected.
_LCD_CURSOR_OFF	Turn off cursor
_LCD_UNDERLINE_ON	Underline cursor on
_LCD_BLINK_CURSOR_ON	Blink cursor on
_LCD_MOVE_CURSOR_LEFT	Move cursor left without changing display data RAM
_LCD_MOVE_CURSOR_RIGHT	Move cursor right without changing display data RAM
_LCD_TURN_ON	Turn Lcd display on
_LCD_TURN_OFF	Turn Lcd display off
_LCD_SHIFT_LEFT	Shift display left without changing display data RAM
_LCD_SHIFT_RIGHT	Shift display right without changing display data RAM

#include "I2C_LCD.h"
#include "built_in.h"

//UChar LCD_01_ADDRESS = 0x7E; //PCF8574A
UChar LCD_01_ADDRESS = 0x4E; //PCF8574T

char txt[] = "Hello World";

void main() {
  int i = 0;
  int j = 1;
  int k = 0;
//CHECON = 0x00;
  TRISE3_bit = 0;
  AD1PCFG = 0xFFFFFFFF;
  JTAGEN_bit = 0;
  I2C2_Init(100000);//INIT I2C AT 100KHZ
  I2C_Set_Active(&I2C2_Start, &I2C2_Restart, &I2C2_Read, &I2C2_Write, &I2C2_Stop,&I2C2_Is_Idle); // Sets the I2C1 module active
  Delay_ms(100);
  I2C_LCD_init(LCD_01_ADDRESS);
  Delay_ms(100);
  I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_FIRST_ROW,1);
  I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_CURSOR_OFF,1); // Cursor off
  I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_CLEAR,1); // Clear display
  Delay_ms(1000);
  i=1;j=0;
  while(1){
        j++;
        i=1;
        I2C_LCD_Out(LCD_01_ADDRESS,j,1,txt);
        if(j > 4){
        j=1;
        }
        while( i < 10){
        Delay_ms(500);
        I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_SHIFT_RIGHT ,1);
        i++;
        }
        while( i > 0){
        Delay_ms(500);
        I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_SHIFT_LEFT ,1);
        i--;
        }
        I2C_Lcd_Cmd(LCD_01_ADDRESS,_LCD_CLEAR,1); // Clear display
  }
}